## Slide 1
Sergey Malygin
Director, Program Management & Solution Delivery
Creating End to End Policy with Flexible Policy Engine
YOTA

## Slide 2
What is Yota?
Yota Phone
Yota Mobile Internet
Yota PCRF

## Slide 3
WiMAX Mobile Broadband
2g / 3G / LTE Data + Voice
LTE Mobile Broadband
Yota Mobile Operator
2008
2014
> 1 million subscribers
AS IT SHOULD BE
Unlimited data tariffs
2012

## Slide 4
Key Drivers & Challenges
Yota is REALLY dynamic company:
    New offers, New DPI, WiMAX -> LTE swap, etc.
Time to Market is CRITICAL!

## Slide 5
Challenges - ACCEPTED
7 cores / RAN Sharing / Multi PCEF: Huawei, Cisco, Procera,
Unified PCC Solution
Advanced Service Model
User features:
      Sliders
      Turbo Button
      Test Drive
      Offers based on device type
Operator features:
      Advanced Policy Control
      Congestion Management
      Online User Interaction
      PCC Notifications to BSS
> 30 regional tariffs > 10 000 km
9 time zones
Russia-wide

## Slide 6
YOTA PCC Architecture
Notes: Поменять шрифт (увеличить)

## Slide 7
Policy Engine
Flexible Policy Engine
BS Load info
Real-time cell load
Subscriber Rating
ANY External Events
Subscriber info:
  Profile
  Services
  Attributes
  Counters
Network session:
Network Events
Usage monitoring
Location/ cell ID
Device type (IMEI)
Schedule & Timers
Date & Time
Day of week
Time accumulation
BI
BSS Provisioning
Core Network

## Slide 8
if service_active("Bronze") then
if not country == 'RU' then -- default country for PCRF installation
log_write(string.format("Subscriber now in %s country", country))
add_rule_static("Roaming")
add_policy("Limited")
return 0
end
if check_accum_level_full("General_Down") then -- no traffic add_policy("Limited")
add_rule_static("Redirect_to_page")
log_write("Subscriber redirected to selfcare page")
return 0
end
if service_active("Turbo") then -- turbo button pressed add_policy("Turbo")
log_write("Turbo button active - add Turbo policy")
else
add_rule_static("Bronze")
log_write(string.format("Add static Gx rule %s", "Bronze"))
end
return 0
Lua
Online or scheduled update
Script debug
Script versions
Fast rollback
Can be applied for dedicated subs or %
HAL (Hardware Abstraction Layer)
Script-based Policy Configuration
Notes: Add animation

## Slide 9
Time 2 Market Benefits
Update subscriber contact information reminder – 3 times OK / CANCEL,
4-th time – CANCEL is not possible
Controlled customer care load – show new offer only for 20% of subs
Notify external system about subscriber authorization in the network
Subscriber home area leave notification to BSS
API for Mobile App: “Should I show the Turbo-button for this subscriber?”
In case of DPI failure perform online fallback for policies enforcement to
P-GW
Idea EVALUATION
1 week - 1 month
1 day - 1 week
Idea IMPLEMENTATION (configure, test and launch)
Notes: Add animation + color

## Slide 10
Availability
99.999%
Performance
15’000 TPS
per 1 node (HP DL360)
Flexibility
Lua Generic Attributes
TimesTen
or
Postgres
Congestion Mgmt
Advanced Service Model
Multi-PCEF
Yota PCRF Benefits

## Slide 11
www.freepcrf.com
SMalygin@yotateam.com
Good for education, evaluation and testing
One-click download for soft & docs
No registration / NDA / SMS, etc.